## Slide 1: ASSESSING PEDESTIRANS’ EXPOSURE TO TRAFFIC NOISE WITH SPATIAL ANALYSIS:
-
Working title
Preliminary methods & results
Joose Helle
THE EFFECTS OF ROUTE CHOICE AND HOME LOCATION

## Slide 2: QUIET PATH ROUTE OPTIMIZATION

## Slide 3: QUIET PATH
Shortest path least cost path
Dijkstra’s algorithm for route optimization
  Utilizes graph theory: networks (graphs) of nodes & edges
  Finds the least cost path between two nodes with respect to edge costs
  If edge cost = length => least cost path = shortest path
  However, edge cost can be any (numeric) attribute
  Here, edge cost should also consider traffic noise

## Slide 4: CALCULATING ADJUSTED EDGE COSTS
= total edge cost
= length of the edge (m)
= additional noise cost of the edge:
= contaminated distance of (e.g. 14 m of 65 dB)
= dB-specific noise cost coefficient (between 0.0–1.0)
= “personal” noise tolerance coefficient (between e.g. 0.1–4.0)

## Slide 5
= 3 m + 7 m + 9 m = 19 m
dB | Noise coefficient ()
45–50 | 0.0
50–55 | 0.1
55–60 | 0.2
60–65 | 0.3
65–70 | 0.4
70–75 | 0.5
75–80 | 0.6
dB | 
45–50 | 0.0
50–55 | 0.1
55–60 | 0.2
60–65 | 0.3
65–70 | 0.4
70–75 | 0.5
75–80 | 0.6

## Slide 6
= 3 m + 7 m + 9 m = 19 m
What nt ?
e.g. 0.1, 0.15, 0.25, 0.5, 1.0, 1.5, 2.0, 4.0, etc.

## Slide 7
QUIET PATH ROUTING
For one routing problem, many alternative (quiet) paths are calculated with different edge costs
Parallel edge costs are calculated with systematically altering nt
  E.g. 0.1, 0.15, 0.25, 0.5, 1.0, 1.5, 2.0, 4.0, etc.
Alternative paths should be compared with respect to:
  Difference in exposures to high traffic noise levels (m)
  Difference in total distance of the paths (m)

## Slide 8: WHAT IS THE BEST PATH ?
Type | nt | Length (m) | Length diff (m) | Length diff (%) | Diff. >60 dB (m) | Diff. >70 dB (m)
short | 0 | 1764 | 0 | 0 | 0 | 0
quiet | 0,15 | 1794 | +30 | +1,7 | -659 | -302
quiet | 1,5 | 1830 | +66 | +3,7 | -675 | -395
quiet | 6 | 2123 | +358 | +20,3 | -937 | -398

## Slide 9: WHAT IS THE BEST PATH ?
Type | nt | Length (m) | Length diff (m) | Length diff (%) | Diff. >60 dB (m) | Diff. >70 dB (m)
short | 0 | 1764 | 0 | 0 | 0 | 0
quiet | 0,15 | 1794 | +30 | +1,7 | -659 | -302
quiet | 1,5 | 1830 | +66 | +3,7 | -675 | -395
quiet | 6 | 2123 | +358 | +20,3 | -937 | -398