## Slide 1: ASSESSING PEDESTIRANS’ EXPOSURE TO TRAFFIC NOISE WITH SPATIAL ANALYSIS:
-
Working title
20.3.2019
Research plan
Joose Helle
THE EFFECTS OF ROUTE CHOICE AND HOME LOCATION

## Slide 2: INTRODUCTION
Active transport modes are considered healthier and more sustainable
  Thus, they are being promoted in many cities
Walking is evidently the most popular active transport mode
However, potential health benefits of walking may get compromised due to the negative effects of vehicular traffic
Vehicular traffic causes pollution which reduces walkability
  Air pollution, noise and visual pollution
  Walkability is a complex concept that aims to consider everything that affects the opportunities for walking
  Safety, utility, comfort, ease, accessibility etc.
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION
Notes: Add ! Visual pollution

## Slide 3
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 4
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION
There seem to be an apparent conflict of interests between road users...

## Slide 5: BACKGROUND
The concept of how different pollutants are experienced by citizens is called exposure
Many of the previous studies on exposures to traffic noise have focused on counting the residents exposed to certain traffic noise levels based on their home location
  Fixed thresholds (dB) have been defined as harmful traffic noise levels
  Also some EU and national legislations require these assessments
  Conceptually straightforward
  Relatively easy to study via spatial analysis: overlay of census data and noise level surfaces
  Static approach ignores the mobility of the residents
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 6
However, true exposure is dynamic
  Daily movements: home location, route selection, etc.
  Used transport modes
More realistic approaches to assess citizens’ exposure to air/noise pollution consider mobility
  Pedestrians & cyclists are most exposed -> emphasis on active transport
  Most citizens are pedestrians every day -> emphasis on walking
Pedestrians’ exposure to pollutants can be quantified as distance or time spent (walking) in areas with different concentrations/levels (of pollutants)
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 7
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION
Exposure as distances at different traffic noise levels along a walking route

## Slide 8
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION
Exposure as durations at different traffic noise levels along a walking route

## Slide 9
At least two approaches for assessing these exposures exist:
  Direct way: using measurement instruments attached to members of a study group and tracking them spatio-temporally
  Indirect way: using spatial analysis to extract modelled concentrations/levels of pollutants to either modelled or tracked paths of people
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 10
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION
Health effects of traffic noise
In many studies, health effects of traffic noise have been assessed
The challenge has often been to separate the health effects caused by the noise from the effects of other environmental factors / pollutants
Yet, it is evident that traffic noise affects citizens physical and mental health in many ways
  Reduced quality of life
  Stress
  Problems in blood circulation (increased blood pressure etc.)

## Slide 11
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 12
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 13
Traffic noise is modelled in many cities with high spatial precision
  Traffic count data & measured noise levels
  Geometries and materials of structures of the environment
  Mathematical equations to assess absorption and transmission of sound in 3D landscape (featuring varying textures, surfaces & geometries)
  Modelled traffic noise data facilitates exposure analysis!
How to minimize the exposure to traffic noise?
  Pedestrian-friendly alternatives are needed to simple shortest paths
  Green/healthy/safe/clean/quiet path routing, as a concepts, aim to take walkability into account in route optimization
    Safety, air quality, noise levels
    Presence of vegetation, green views
    Other environmental variables that affect walkability
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 14
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 15
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 16
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 17
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 18
Route optimization algorithms can be used to find shortest paths in a network (graph)
  Utilizes graph theory: navigable networks of nodes and segments (connections) (e.g. network of streets & intersections)
  e.g. Dijkstra’s algorithm finds the shortest path between nodes in a graph
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 19
Usually lengths of the segments are used as the costs
Real-world applications usually require more complex graphs
  Directed graphs
  Intersection costs
  Speed limits
  Custom weights
    Walkability
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 20
Exposures to pollutants at different parts of the network can be used as additional weights in the shortest path analysis
  Noise levels (or air pollutions) are assigned to street segments of the network (spatial join) -> network of “contaminated distances”
  Environmental impedance function is needed to convert the contaminated distances into weights usable by the route optimization algorithms
  -> More pedestrian-friendly routes
  Challenge is often the validation and definition of thresholds for different pollutants
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 21: AIMS OF THE STUDY
Develop a “quiet path” routing method/tool that optimizes more pedestrian-friendly walking routes by minimizing exposure to traffic noise pollution
Explore spatial patterns in pedestrians’ exposure to traffic noise on the walking legs of public transport itineraries to workplaces and to local grocery stores:
  Which residential areas accumulate the highest pedestrians’ exposures to traffic noise?
  How the opportunities to choose healthier (less noisy) walking routes are distributed spatially?
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 22: AIMS OF THE STUDY
Publish the developed methods as a pilot/proof-of-concept (POC) quiet path planner app
  User can plan more pedestrian-friendly walking routes
  Web map application: client-side interactive web map + server-side routing service
  For each routing query, several alternative routes are returned from the server and visualized on the map
    Information of route length and exposures to different noise levels along the route are also shown
Explore opportunities to implement the quiet path routing in HRT’s route planner
  It’s open source and uses OpenTripPlanner (OTP)
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 23: MATERIALS
Modelled Traffic noise zones in Helsinki 2017
  Urban Environment Division of city of Helsinki
  WFS Service: spatial data in surface/polygon format
  Noise range information as attributes (45-50, 50-55 dB etc.)
OpenStreetMap (OSM)
  Data will be acquired programmatically using Overpass API
  Tag ‘highway’ is used to get all road segments
  Walkable street segments are filtered from the data (based on tag-key -value pairs) and used in the network construction
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 26
Digitransit Routing API
  Used to query the routes from residential areas to workplaces
  Walking legs of the planned itineraries (routes) are used in the exposure analysis
YKR Population grid
  250m x 250m polygon grid layer
  Centers of the grid cells are used as origins in the routing analysis
  Cumulative exposures are aggregated by the origin grid cells
YKR Workplace grid
  Centers of the grid cells are used as destinations in the routing analysis
Grocery stores
  Walking routes are also calculated from each origin cell to the closest grocery store for exposure analysis
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 27: METHODS
Acquiring and processing walkable street network
Query walkable OSM edges from Overpass API
Use OSMnx* to convert OSM data into (NetworkX*) graph
Extract & assign traffic noise levels to all segments of the network as attributes
* Python library
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 28
Itinerary planning from all origins to their respective workplaces
Query planned itineraries from Digitransit Routing API
Extract first walking leg of each planned itinerary (origin - PT station/destination)
Aggregate origin-PT station/destination pairs
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 29
Shortest paths and exposures to traffic noises
Calculate shortest paths for each origin-PT station pair
Calculate shortest paths for each origin– closest grocery store pair
Extract & join exposure to traffic noise to each walk
Aggregate exposures to traffic noise at origin level (mean, median etc.)
Visualize results (maps & figures)
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 30
Calculating “quiet paths” by minimizing noise exposure
Assign additional cost to network segments with environmental impedance function: Personal noise tolerance (PNT) * traffic noise levels * length
Calculate shortest paths with respect to additional noise impedances
Compare paths to shortest path (distance & noise exposure)
Adjust PNT and repeat...
Visualize results (maps & figures)
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 31: TECH
Only open source tools & libraries will be used
  Python development environment managed with Conda
  Geopandas, Shapely, OSMnx, NetworkX for spatial analysis and network construction
  QGIS for the visualizations
Static files for storing data and results
  GeoPackages might outperform Shapefiles when handling large files with Geopandas and QGIS
  Probably no need to use databases for performance or due to very large datasets
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 32
More computing power from CSC if necessary
  Parallel processing with Python?
  At least for network construction, noise data extractions for segments and route optimizations (shortest paths)
  servicedesk@csc.fi ?
Reproducibility and quality assurance
  No manual/undocumented steps in the analysis
  Unit tests for most important functions
  All codes shared in GitHub (already now: github.com/hellej/gradu-pocs)
  Simple one line setup / configuration for identical Python environment as used in the study (with Conda)
Functions should be modularized to be useful also in assessing exposures to other pollutants
  Highly modularized and well documented codebase (not yet)
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 33
The “quiet path” routing as a proof of concept (POC) web app
    Route optimization service as a server-side application featuring REST API built with Python + Flask/Django (?)
    User interface as a front-end web map application built with ReactJS & Mapbox GL (?)
    Minimum viable product
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 34
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION
Architecture of the quiet path routing web app:

## Slide 35: EXPECTED RESULTS
Higher exposures to traffic noise in some areas
  Massive road infrastructure, high (vehicular) traffic flows
  Long distances from residential areas to PT stations / grocery stores
  Exposed walkways near big highways
  Low walkability?
Lower exposures to traffic noise in other areas
  Good walkable street network: sheltered and functional walkways
  Short distances to PT hubs
  Low traffic flows
  Residential streets as opposed to big highways
  Better walkability?
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 36
Opportunities for choosing healthier (less noisy) walking routes are distributed unequally:
More / better opportunities are found in areas where
  Noise exposures along the shortest paths are high (also the potential to reduce them is higher)
  Sheltered walkways exist and are well connected to the rest of the street network
  The walkable street network is dense and hence total number of route options is greater
Less opportunities are found for areas where:
  Noise exposures along the shortest paths are already low
  No sheltered walkways exist or they are not well connected to the rest of the street network
  Sparser network doesn’t provide many route options in the first place
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 37: DISCUSSION
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION
More realistic approach to assess citizens’ exposure to air/noise pollution is to also consider their mobility
Spatial analysis can provide estimates of pedestrians’ exposures to traffic noise with limited accuracy
  Real “taken” paths are likely to differ from the modelled (shortest) ones
  Real traffic noise levels vary in time
”Quiet path” routing is sensitive to definition of the environmental impedance function
  Weighting of varying exposures to different traffic noise levels is subjective and hence tricky
  Hence, the sensitivity of the quiet route optimization needs to be evaluated by systematically altering the environmental impedance function

## Slide 38
Both exposure to traffic noise and the presence of alternative (better) walking routes need to be known in order to support spatial planning
  Exposure to noise along only the shortest path is not enough
  Exposure to noise along the alternative (short) paths is essential
  If exposures to noise are high both along the shortest and the alternative paths (if any), actions should be crafted to improve opportunities for walking in the area
Quiet path routing method needs to be published in order to improve citizens quality of life
  Nothing but a static python script collecting dust in a GitHub repository doesn’t help anyone to choose better walking routes
  Hopefully the implementation of the interactive web map route planner application is feasible enough
  ...Or that HRT implements something similar in their route planner
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION

## Slide 39: SCHEDULE
Gathering literature
  January - March
Data processing and analysis
  March – April
Visualizations and writing
  April – May
Done?
  June
INTRODUCTION ▶︎ BACKGROUND ︎▶ AIMS OF THE STUDY ▶ MATERIALS & METHODS ▶ EXPECTED RESULTS ▶ DISCUSSION