## Slide 1: ASSESSING PEDESTIRANS’ EXPOSURE TO TRAFFIC NOISE WITH SPATIAL ANALYSIS:
-
Working title
Preliminary methods & results
Joose Helle
THE EFFECTS OF ROUTE CHOICE AND HOME LOCATION

## Slide 2: QUIET PATH ROUTE OPTIMIZATION

## Slide 3: LEAST COST PATH
Shortest path least cost path ?
Dijkstra’s algorithm can solve both
  Utilizes graph theory
  Nodes & edges
  Finds least cost path between two nodes based on edge attribute containing cost
  If cost = length => least cost path = shortest path
  Here, cost should also consider traffic noise

## Slide 4: CALCULATING ADJUSTED EDGE COSTS
= total edge cost
= length of the edge (m)
= additional noise cost of the edge:
= contaminated distance of (e.g. 14 m of 65 dB)
= dB-specific noise level cost coefficient (between 0.0–1.0)
= “personal” noise tolerance coefficient (between e.g. 0.1–4.0)

## Slide 5
= 3 m + 7 m + 9 m = 19 m
dB | Noise coefficient ()
45–50 | 0.0
50–55 | 0.05
55–60 | 0.1
60–65 | 0.2
65–70 | 0.3
70–75 | 0.4
75–80 | 0.6
dB | 
45–50 | 0.0
50–55 | 0.05
55–60 | 0.1
60–65 | 0.2
65–70 | 0.3
70–75 | 0.4
75–80 | 0.6

## Slide 6
= 3 m + 7 m + 9 m = 19 m
What nt ?
e.g. 0.1, 0.15, 0.25, 0.5, 1.0, 1.5, 2.0, 4.0, etc.

## Slide 10: HOW TO COMPARE ALTERNATIVE PATHS ?
Type | nt | Length (m) | Length diff (m) | Length diff (%) | Diff. 60 dB (m) | Diff. 70 dB (m)
short | 0 | 1764 | 0 | 0 | 0 | 0
quiet | 0,15 | 1794 | 30 | 1,7 | -659 | -302
quiet | 1,5 | 1830 | 66 | 3,7 | -675 | -395
quiet | 6 | 2123 | 358 | 20,3 | -937 | -398